## Slide 1
Week 4: Rivers as Conveyors (Fluxes of water, sediment, and elements)
The Water:
Measuring and Monitoring Discharge (Q):
  Besides apples, how do we accurately measure Q?
  Long-term monitoring of Q.
  Channel Roughness and Manning’s Equation.
  Bankfull discharge - identification and prediction.
The Stuff in the Water:
Sediment and element loading:
  It goes where the water goes.
  How do we measure how much is in the water?
  Erosion and sediment loads

## Slide 2
Start with the water:
Discharge (Q) m3/sec

## Slide 3
Stream Gauging:
Discharge has been recorded since the Egyptians:
(flooding along the Nile)
How are precipitation and river level related?
Precipitation
Event
(hyetograph)
River Discharge
Response
These relationships are specific to each individual basin

## Slide 4
1870
2007
LS00878 and LS11203_001 from the Landscape Change Program
Q (Discharge)
Time
Base flow

## Slide 5
Flow Gauging:
Things we want to figure out:
How much water is flowing through a river cross-section
At a particular instant in time?
2. At a certain discharge, how deep will the water be?
Q = A x V
What we need to answer these:
Detailed cross-section of channel Geometry
AND Velocity across that cross-section
2. Multiple paired Q-d measurements

## Slide 6
1
Surveying River Cross-Sections:
Width
Water Depth
Velocity

## Slide 7
Surveying River Cross-Sections:
Depth (m)
Distance (m)
Water level
Q
Q
Width x Ave Depth x Velocity = Cruddy Q

## Slide 8
Need Much More Detail: Divide into Sections
Depth (m)
Distance (m)
Water level
1
2
3
4
5
6
7
3
Width
Average Depth
Velocity Measured
At 0.6 depth at mid-point
When you are done, you add up all the sections to get the
Total Discharge for the entire channel

## Slide 9
Flow meter for measuring water speed
1
.6d

## Slide 10
Critical to make a sketch of your cross-
Section as you go.
This is where you catch all your mistakes

## Slide 11
1
Do enough of these, and you can make a
Stage Height Discharge Rating Curve
Q
Water Height
Predict River
Stage for any Q.
Good for flood
prediction

## Slide 12
Why does the curve “Roll” over?

## Slide 13
Hydro + geomorph = flood zone mapping
Notes: Geomorphologists informing society

## Slide 14
Channel Roughness
Manning Equation:

## Slide 15
Manning Equation:
represents the roughness or friction applied to the flow by the channel
A = cross-sectional area (m2)
R = Hydraulic Radius (a/WP) (m2/m)
S = Slope (m/m)
N = Manning n (roughness coefficient)
Bigger the n, the rougher the channel is
Watch
Units
Q and n inversely related…one goes up, the other must go down. LWD?
Notes: Irish engineer Robert Manning 1889 assumes uniform flow

## Slide 16
R - Hydraulic Radius
R = Hydraulic Radius (a/WP) (m2/m)
Cross-sectional Area of river channel / Wetted Perimeter
(the data you will collect) (WP ~ width + 2depth)
(square meters) (meters)

## Slide 17
S - Slope of WATER SURFACE
Run
Rise
Slope = change in elevation / distance downstream
(rise) (run)

## Slide 18
2
Manning n values:

## Slide 19: http://wwwrcamnl.wr.usgs.gov/sws/fieldmethods/Indirects/nvalues/
Clark Fork at Missoula, Montana
n = 0.030
Boundary Ck at Porthill, Idaho
n = 0.073
2

## Slide 20
Why would anyone care how rough or smooth
A river channel is?
“smooth channel”
“rough channel”
Water level
Water level
Same Q
Same Q
Relative velocity?
Higher Stage

## Slide 21
Bank full flow about
Once every 1-2 years
Try to define in field using
observations
3
“Channel-forming flow”?
This is for alluvial channels
Flow Levels

## Slide 22
Identifying Bankfull in the Field
(Here’s where it gets interesting)
Break in slope
Inset bench or small terrace
Vegetation change
*Combine with Mannings n to predict Q
Bankfull!

## Slide 23
The Stuff in the water:
Sediment mass loading in rivers:
Sediment load: The mass of sediment carried in
The water column at a particular discharge and at a particular
Point along a river channel (mass / volume)
Sediment Yield: The total mass of sediment yielded per unit
Area per time (e.g. Tons / km2 / yr).
Changes downstream
Changes with discharge

## Slide 24
Bedload -- material moving along the bed, shear forces exerted by water sufficient to move clasts -- rarely measured (at % level)
Suspended Load -- material kept in the water column by turbulence and lift forces (easy to measure in grab samples)
Bedload usually <<< than suspended load and ignored
Dissolved Load -- material in solution (easy to measure in grab samples)
Dissolved load varies, usually < than suspended load
4
Sediment Transport Through Rivers

## Slide 25
4
Sampling for Suspended Load……
Optical Sensors

## Slide 26
Integrate suspended load over all flows (mass/time)
Integrate bedload load over all flows (mass/time)
Integrate dissolved load over all flows (mass/time)
+
+
Getting from daily sediment yields
To total mass loading and erosion rates
Typically, measured kg of sediment each day, added together over
An entire year.
=
TOTAL MASS LOSS (mass/time)
Divide by density and can express as Height change/time m/My…..cm/ky

## Slide 27: Load varies over time and discharge

## Slide 28: Integration over all flows is a non trivial problem! Need Rating Curves (suspended, dissolved, bedload)
4
Suspended Load - Similar to Discharge Curves
Suspended Sediment concentration
Discharge
Can predict
Concentration
At any given
Discharge

## Slide 29: Integration over all flows is a non trivial problem! What happens when you track through the hydrograph
4
Hysteresis loop:
Sediment concentration
Different at the same
Discharge.
Make predicting
Concentration based
On discharge difficult
Suspended Sediment concentration
Discharge
Hydrograph

## Slide 30: SEDIMENT YIELD - What comes out
SEDIMENT GENERATION - Material generated by weathering and erosion
= or ≠
Timescale
Steady state
Human impact
Episodic disturbance

## Slide 31
Where Did Irene Dump our Real Estate?

## Slide 32: River Lab Logistics
On Huntington, in water
Measure discharge - river surveying and velocity measurements
Compare pools and riffles - Discharge and Roughness.
Field estimate of bankfull stage - Need channel geometry and slope
Suspended and dissolved load on Wednesday.
Bring: Raingear, warm clothes, pencils and waterproof paper
OLD TENNIS SHOES! Teva/toenail story

## Slide 33
http://www.youtube.com/watch?v=4LxMHmw3Z-U&feature=related