## Slide 1
25+ Years of Acid Deposition Monitoring in Vermont
  (2) Citizen Acid Rain Monitoring Networks (LCC+UVM and Audubon)
  Vermont Acid Precipitation Monitoring Program
  Utility Acid Precipitation Study Program
  EPRI Operational Evaluation Network
  Atmospheric Integrated Research Monitoring Network (Wet & Dry)
  Clean Air Status and Trends Network (Dry)
  National Atmospheric Deposition Program - National Trends Network

## Slide 2
  National Atmospheric Deposition Program - National Trends Network
  263 Currently Active Sites, Primarily in US, but also Canada, V.I. P.R., Argentina

## Slide 3
Underhill NADP Site VT99
Established 6/12/1984
Bennington NADP Site VT01
Established 4/28/1981
PRISM Model Estimated 2013 Precipitation Amount (Parameter-elevation Relationships on Independent Slopes)

## Slide 4
The pH of VT precipitation has increased from
4.3 to 4.4
in the 1980s
To
5.0-5.1
in 2014
An 80% reduction
of acidity in the past 30 years

## Slide 7
Chart: 3-Year Average Underhill Wet Nitrogen Deposition from Nitrate and Ammonium
| 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
NO3 N Deposition | 3.2116 | 3.7716 | 3.6979 | 3.7611 | 3.9252 | 3.8883 | 3.5127 | 3.5865 | 3.7325 | 3.8326 | 3.311 | 3.2335 | 3.5902 | 3.542 | 3.4743 | 3.1281 | 3.2974 | 2.9888 | 2.9956 | 2.7359 | 2.7058 | 2.5719 | 2.4861 | 2.2783 | 2.0141 | 2.0412 | 2.1699 | 2.2783 | 2.2076
NH4 N Deposition | 1.6504 | 1.9455 | 1.7633 | 1.8634 | 1.9866 | 2.1791 | 1.9378 | 1.8249 | 2.1047 | 2.292 | 2.1355 | 1.9558 | 2.174 | 2.0764 | 2.0662 | 1.8454 | 2.2279 | 2.1355 | 2.3254 | 2.0687 | 2.0354 | 2.1226 | 2.1894 | 2.2612 | 2.1971 | 2.2484 | 2.4101 | 2.3126 | 2.3793

## Slide 8
NADP Concentrations Combined with PRISM Topo-enhanced Precip. Volume to produce Gridded (4 km) Wet S & N Deposition Data
Available 1985-2014
CMAQ Modeled S & N Dry Deposition Data enhance/adjusted to (sparse) measurements for Gridded (12 km) Dry S & N Deposition Data Available 2000-2013
Combined Gridded (4 km) Total Deposition Data
S: 55% to 81% Wet in 2000
S: 36% to 71% Wet in 2013
N: 36% to 71% Wet in 2000
N: 36% to 79% Wet in 2013
Available 2000-2013
2000 Wet S Deposition + 2000 Dry S Deposition = 2000 Total S Deposition

## Slide 9
1985 Wet NO3 Deposition 2013 Wet NO3 Deposition

## Slide 10
1985 Wet SO4 Deposition 2013 Wet SO4 Deposition
Thanks to Bennet Lyon (the New Bennington NADP Site Supervisor) for the Maps!