## Slide 1: Defining and Targeting High Flows
Vermont Monitoring Cooperative Conference
December 2, 2016
South Chittenden River Watch

## Slide 2
River | Drainage Area (sq. mi.) | Impacts on Water Quality
LaPlatte River | 46.36 | Rural, receives treated effluent in Hinesburg
McCabe’s Brook | 4.59 | 
Middle Segment | 1.47 | Agricultural
Downstream Segment | 1.21 | Town of Shelburne storm water
Thorp Brook | 2.93 | Agricultural
Kimball Brook | 1.87 | Agricultural
SCRW Monitoring Program - Watersheds

## Slide 3
1. Phosphorus Burdens Associated with Suspended Solids

## Slide 4
River | Apparent “Threshold”/ “Critical” Flow (cfs) | % of Mean Daily Discharge Values Less than or Equal to Threshold Flow (cfs) | Period of Record
LaPlatte River | 100 | 87.5 | 1990-2010
Lewis Creek | 450 | 96.7 | 1990-2014
Little Otter Creek | 95 | 83.6 | 1990-2006
Otter Creek | 2,000 | 82.7 | 1990-2006
McCabe’s Brook | 5 | 85 | 2012-2013
Comparison of “Critical” Discharge Rates in the
LaPlatte Watershed and Addison County Streams

## Slide 5
2. Particle Size Analysis

## Slide 6
3. In-stream Phosphorus Mass Balances

## Slide 7: McCabe’s Brook: A Losing Stream
Many mass failures, gravel deposits, dry beds:
  At low flows water flows through gravel, stream may disappear
At low flows, downstream segment often receives now flow from upstream catchment
Upstream nutrient loadings at times exceed downstream loadings

## Slide 8
4. Events Associated with High Flows

## Slide 9
5. Loading Rates by Discharge Classes
Median Phosphorus and Solids Loading Rates (Kg/Day) in McCabe’s Brook at Harbor Road (SCRW Data 2011-2014) |  |  |  | 
Discharge Class Interval | Phosphorus |  |  | Total Suspended Solids
 | Total | Particulate | Dissolved | 
<1 cfs | 0.10 (5) | 0.07 (4) | 0.05 (4) | 23.98 (5)
1-5 cfs | 0.32 (11) | 0.16 (11) | 0.21 (11) | 75.99 (11)
5-10 cfs | 2.94 (4) | 1.24 (4) | 1.56 (4) | 638.09 (4)
>10 cfs | 7.36 (2) | 5.35 (2) | 2.01 (2) | 3,224.41 (2)

## Slide 10
Rough Estimate of % of Total Load Discharged from McCabe's Brook
when Stream Discharge Rates Exceeded 5 cfs
(May 30 to November 11, 2012; May 27 to October 14, 2013)
 | 2012 | 2013
Days of Record | 170 | 137
Phosphorus: |  | 
Total | 14 % | 86 %
Particulate | 18 % | 89 %
Dissolved | 7 % | 75 %
Total Suspended Solids | 23 % | 92 %

## Slide 11: Conclusions
High flow monitoring requires effort, but has proved feasible
Discharge at the USGS gage on the LaPlatte River has proved a reasonable indicator of discharge in adjacent watersheds
In-stream flow measurement is informative, but not affordable on routine basis
High flow monitoring can pick up events impacting on in-stream water quality and loadings on Lake Champlain
High flow monitoring targets flows representative of entire watersheds providing a better picture of entire watersheds
High flow monitoring tracks the most meaningful data relating to nutrient and sediment loadings on Lake Champlain

## Slide 12
Final Questions
Does high flow monitoring present a more
meaningful picture of potential impacts on
receiving water bodies than does random
flow monitoring?
Can high flow monitoring improve our
ability to detect and understand change
over time?

## Slide 13: THE END