## Slide 1: Progress towards high-throughput sequencing for clinical HLA genotyping
Matthew W. Anderson MD, PhD
Assistant Professor, Department of Pathology
Assistant Director, Stanford Histocompatibility, Immunogenetics, and Disease Profiling Laboratory (HIDPL)
Stanford University School of Medicine

## Slide 2: Conflict-of-interest disclosure
Sponsored research:
Roche (454 study)
Life Technologies

## Slide 3: Potential benefits of next-generation sequencing for clinical HLA genotyping
Clonal template amplification in vitro to eliminate problem of sequencing heterozygous DNA
Potential for one-step high resolution typing
Increased sequence coverage of HLA genes
Capability to multiplex specimens
Reduce turn-around-time

## Slide 4: Outline
Roche multi-site trial
Ongoing development efforts
  Sequencing workflow improvements
  Amplicon genotyping
  Shotgun sequencing

## Slide 5: Roche 454 HLA study
Designed to evaluate feasibility/reproducibility
of using the Roche 454 sequencing platform to
perform HLA typing in the clinical laboratory
  Two independent pilot studies had previously demonstrated the power of this approach
  Eight participating laboratories
  20 double-blinded samples with difficult SBT results (rare alleles, etc) submitted for analysis
  Laboratories trained to perform experiment independently
Holcomb CL, et al., Tissue Antigens 2011, 77: 206-217.

## Slide 7: Results: study group
Raw data:
  Average sequence read 250 bp
  672 sequence reads per amplicon
Allele assignments were made in 95% of cases
  Missed calls due to novel alleles or technical errors
  Manual editing performed for only 3.7% of loci
  57% of cases had residual ambiguity
Concordance between sites was high (95.3% - 99.4%)
Concordance with known alleles was 98.3%

## Slide 8
Result example

## Slide 10
Novel allele (DQB1 exon 3 variant)

## Slide 11: Amplicon genotyping workflow
Designed and validated primers for HLA Class I exons 1-7 and 2-3 for Class II exons
Adapted Access Array for multiplexed HLA amplicon library generation
Optimized library purification steps
Developed performance metrics to monitor all steps of sequencing process for Q/C
Sequence generated using a 454 GS Jr instrument
Collaborating with Conexio Genomics to develop custom bioinformatic pipeline

## Slide 12
Tagged sequence-specific primers (up to 48 individual targets)
Barcode primers and up to 48 individual samples
Exon
Intron
Intron
Up to 48 barcoded amplicons from each sample (up to 2,304 amplicons)
Extract DNA
Purify sequencing templates
Sequence
Emulsion PCR
Pool amplicons
Dilute amplicons
Quantify amplicons
Purify amplicons
Genomic PCR
Analyze using Conexio
Generate final report
Extract DNA
Purify sequencing templates
Sequence
Emulsion PCR
PCR using Access Array
Analyze using Conexio
Generate final report
Automate using robotics and emulsion purification device

## Slide 13: Library prep with Access Array
Amplify 24 patients with 22 primer sets simultaneously
Allows for one-step barcoding of amplified products
Can “double-up” on reactions to increase total amount of product generated
Allows for easy recovery of amplified barcoded products
Can pool barcoded amplicons from different patients together without need for manual quantification and dilution of each individual amplicon

## Slide 16: Shotgun sequencing workflow
Designed and validated long-range PCR primers to amplify DQA1 gene
Sequencing library prep using chemical cleavage and size selection
Data analyzed in collaboration with Chunlin Wang (Stanford Genome Center)
Collaborating on analysis with Conexio Genomics

## Slide 17
*01
*02
*03
*04
*05
*06
NC
DQA1 LR-PCR results

## Slide 18: Sequencing workflow
Ex 3
Ex 4
Ex 1
Ex 2
Fragmentation
Ligate barcoded adaptors
Size select and purify 300-340 bp fragments

## Slide 19
Sequencing library Q/C
Ex 3
Ex 4
Ex 1
Ex 2

## Slide 22
Wang, C. et al., PNAS 2012, 109 (22):8676.

## Slide 23
Case # | Type 1 | Type 2 | PGM 1 | PGM 2
87050 | 01:02 | X | 01:02:01:01 | 01:02:01:01
78384 | 01:GN | X | 01:01:01 | 01:01:01
78412 | 01:GN | X | 01:01:01 | 01:01:02
87121 | 02:01 | X | 02:01 | X
81452 | 02:01 | X | 02:01 | X
84921 | 02:01 | X | 02:01 | X
79677 | 03:01 | 03:MN | 03:01:01 | 03:03:01
80593 | 03:MN | X | 03:01:01 | X
83796 | 03:MN | X | 03:01:01 | 03:03:01
84775 | 04:01 | X | 04:01:01 | X
77591 | 04:MS | X | 04:01:01 | X
84424 | 04:01 | X | 04:01:01 | X
80862 | 05:AXPF | X | 05:05:01:01 | X
82057 | 05:EF | X | 05:05:01:01 | X
83537 | 05:BFK | X | 05:05:01:01 | X
84514 | 06:01 | X | 06:01:01 | X
51387 | 06:01 | X | 06:01:01 | X

## Slide 24
Case # | Type 1 | Type 2 | PGM 1 | PGM 2
76330 | 05:03 | 05:05 | 05:03 | 05:05:01:01
76390 | 03:MN | 04:MS | 03:01:01 | 04:01:01
79014 | 01:MV | 06:01 | 01:01:01 | 06:01:01
77524 | 02:01 | 05:EF | 02:01 | 05:05:01:01
82980 | 01:03 | 04:01 | 01:03:01:01 | 04:01:01
78084 | 01:GN | 02:01 | 01:01:02 | 02:01
77127 | 03:BC | 05:EF | 03:03:01 | 05:05:01:01
81871 | 01:MV | 05:01 | 01:04:01:01 | 05:01:01:01
03:MN=01/02/03 04:MS=01/02/04 01:MV=01/04/05 05:EF=05/09
01:GN=01/04/05/07 03:BC=02/03

## Slide 25: Ongoing development efforts
Amplicon workflow:
  Further optimizing Access Array and emulsion PCR conditions to ensure even coverage of all amplicons
  Improving primer design to reduce pseudogene amplification
  Collaborating with RMS on improved primer sets
Shotgun workflow:
  Experimenting with additional primer sets
  Expand sample size
  Working with multiple informatics platforms
  Planning to extend approach to other loci

## Slide 26: Acknowledgements
Stanford Histocompatibility, Immunogenetics, and Disease Profiling Laboratory
  Heidi Farina
  Fiona Yamamoto
  Dolly Tyan
  Marcelo Fernandez-Vina
Life Technologies
  David Dinauer
  Carolyn Bialozynski
  Steve Berosik
Conexio Genomics – Damian Goodridge
Stanford Genome Center
  Chunlin Wang
  Sujatha Krishnakumar
  Michael Mindrinos
Roche Molecular Systems
  Henry Erlich
  Cherie Holcomb
  Bryan Hoglund